## Slide 1: Air quality in Delhi, India
Aidan Frederick, Ben Walter, & Kyle Maher

## Slide 2: Why Delhi?
The City of Delhi is one of the world's most populous cities
  34.7 million people within only 1,484 square kilometers
  Results in 29,000 people per square mile
With so many people in one space, a few questions arise:
  How significant is air pollution in Delhi?
  When is it at its least and greatest for any given season?
  What circumstances affect these values?
  How is air quality projected to change?
https://worldpopulationreview.com/cities/india/delhi

## Slide 3: Continuous air quality monitoring stations
Station Chosen for Analysis:
  North Campus, DU, Delhi
Rational:
  Several years of relatively consistent data
  Located on a university campus
  Dense population surrounding the station
https://www.mdpi.com/2073-4433/13/12/2090

## Slide 4: Selecting a Parameter
Correlation Insights:
  High concentrations of CO, NO, NO2, NOx, PM2.5 and PM10 occur at the same time
  High concentrations of Benzene, Toluene, and Xylene occur together
    Linked to car emissions
Parameter focus: PM2.5
  Represents concentration of particulates that are less than 2.5 micrometers in diameter
  Exposure is linked to:
    Aggravated asthma
    Decreased lung function
    Increased respiratory symptoms
    Difficulty breathing
  World Health Organization recommended limit
    Daily Average: 15 μg/m3
    Annual Average: μg/m3
https://www.epa.gov/pm-pollution/health-and-environmental-effects-particulate-matter-pm
https://smartairfilters.com/en/blog/who-updates-air-quality-pollution-guidelines/?srsltid=AfmBOoqbp1QL4WJ8VLsTe03reEG0aoykdb1SQHJ0gm2tYN5swiW4Krct

## Slide 5: Particulate Sources
The following influence air quality in Delhi:
  Stoves
  Vehicles with modified fuel
  Idling Vehicles
  Field burnings after harvest
  Celebrations and Festivals
  Livestock
  Dust storms
  Badarpur Thermal Power Station
https://www.iqair.com/us/india

## Slide 6: PM2.5 Recommended Limits, and Delhi
The World Health Organization recommends PM2.5 levels below 15𝑢𝑔/𝑚3 for a daily average and below 5𝑢𝑔/𝑚3 for a yearly average.
Plotted below are those limits with respect to our PM2.5 data.
Delhi sees frequent periods of PM2.5 values far exceeding the WHO's recommendations.
Summer months tend to have the values closest to safe limits while the late fall and winter months see the highest spikes.

## Slide 7: Achieving Stationarity
Log transformation outputs near stationary series
  Variance remains changing
Box-Cox transform returns effectively stationary data
  Decreasing but mostly stable variance

## Slide 8: Initial Hourly Modeling Attempts
ARIMA Model
  Resulted in extreme forecast prediction intervals
Neural Network Model
  Also resulted in extreme forecast prediction intervals
STL with ETS
  Issues with missing values
  Mean Imputation
    Also resulted in extreme forecast prediction intervals

## Slide 9: Diwali Festival
The yearly Diwali celebration generally results in a spike in particulate levels due to fireworks, candles, and thrown gulal (colored powder)
  Influence accounted for with a dummy variable

## Slide 10: Crop Burning Season
Crop burns in Delhi occur between September and November and result in a predictable spike in air particulates before winter
  Influence accounted for with a dummy variable

## Slide 11: The Prophet Model
Due to the presence of multiple layers of seasonality, only the Prophet model could handle hourly data
  However, the model returned exceptionally high RMSE and MAPE values
    MAPE: ~96% suggests that this model poorly represents the data
The Forecasts routinely underestimate PM2.5 values during Diwali and burn seasons.
Point estimates have significantly less variance compared to real data points in general
The Prophet model is unlikely to be the best forecasting choice

## Slide 12: Predicting Weekly Data
Change in Strategy:
Aggregated the hourly data to weekly
  Eliminates daily seasonality, making data easier to work with and yielding better results
A train-test split was implemented (80%-20%)
Interpolation:
STL/ETS models require no missing values in the data
  Estimated missing values in data using a Dynamic Harmonic Regression (DHR) Model
    K = 7 Fourier paired terms
Models Generated:
STL/ETS Decomp: constrained positive with log(PM2.5) data
Neural Network Autoregression: 3 lagged inputs, 1 yearly seasonal input, and 2 hidden nodes
DHR: K=6, with ARIMA(0,1,2)(1,0,0)[52] errors
  First differenced data, second order MA component
  First order seasonal AR component (yearly)
Combined Model:
  Average of the predictions of the 3 models above
  Bootstrap 1000 sample paths into prediction intervals

## Slide 13: Comparisons and Final Model Choice
Combination and STL models best mirror data visually
DHR model has the widest intervals and worst distributional forecasts
Choosing a Model:
Combined and DHR models have highest point accuracy (RMSE/MAPE)
DHR distributional forecasts are far worse than the Combination model's (CRPS)
Final Choice: Combination Model
Model | RMSE | MAPE | CPRS
DHR | 26.1 | 28.6 | 61.3
Combination | 26.8 | 26.7 | 13.6
STL/ETS | 28.1 | 28.8 | 16.0
NNAR | 40.7 | 33.9 | 19.3

## Slide 14: Final Forecasting
Combination model forecasts of 104 weeks, or roughly 2 years producing the following:
PM2.5 air pollution is projected to decrease slightly from 2023-2025,
  An increase is within our prediction intervals.
The lowest estimate in August of 2023
  33.15853 𝜇𝑔/𝑚3
  Still above the WHO's safe daily limits.
Highest estimate occurs in December of 2023
  189.5962 𝜇𝑔/𝑚3
  Exceeds any safe values

## Slide 15: summary
Raw Data
  Hourly PM2.5 concentration from September 2017 to March 2023 in Delhi, India
Data Processing
  Box-cox transformation required to stabilize the variance
Initial Problems
  The standard models could not make forecasts within reasonable prediction intervals at the hourly level
Improvements
  Weekly aggregation removed daily seasonality allowing for the standard models to be used effectively
  The Combination model built from the average of STL/ETS, DHR ARIMA, and Neural Net forecasts performed best
PM2.5 Forecasts from the Combination Model
  A slight decrease is projected by the point forecasts
  A significant increase remains within the forecast prediction intervals
  Extreme seasonality is expected to continue
Air pollution in Delhi remains a significant problem for Delhi residents
  Even the generous side of the forecast prediction intervals show many days far above the WHO’s recommended limit

## Slide 16: Q & A

## Slide 17: Thanks